## Slide 2
Focal problem: global position estimation
  de-facto standard: Global Navigation Satellite Systems (GNSS) such as GPS, GLONASS, Galileo
  problems with GNSS: intentionally disturbed signals and reflected signals within street canyons or natural landscape features
Reduced problem tackled in this work:
  assume to be located on a street network represented as a 3d map
  exploit odometry, barometer, and compass measurements within particle filter framework to answer the question: where am I?
Introduction | World Model | Particle Filter | Evaluation
Introduction

## Slide 3
Road Network: OpenStreetMap (OSM) data
  based on user-recorded GPS track logs
  XML vector representation with classification of road types
OSM data stored in PMR-Quadtrees
  space partitioning data structure sorting its entries into buckets
  bucket is split into four child buckets when |entries| exceeds threshold c
  let N := |position hypotheses| and M := |road segments| ↓ (c*N) instead of (M*N) distance(road segment, position) queries for finding closest road segment to given position hypothesis when using PMR-Quadtree
Introduction | World Model I | Particle Filter | Evaluation
World Model I

## Slide 4
Digital Elevation Model: Shuttle Radar Topography Mission (SRTM) Data
  covers earth’s surface between 60°N and 57°S
  square resolution: 3 arcsec (~90m) standard 1 arcsec (~30m) USA
  max relative vertical error: ±6m within 200 km
  max absolute vertical error: ±16m for all measurements
  void data points can be found over water bodies and mountainous regions
  90m-tiles covering 1° lon * 1° lat are freely available to the public and shipped as 1201*1201 data points of 2 bytes each
TICC
Introduction | World Model II | Particle Filter | Evaluation
World Model II

## Slide 5
Estimated state is a pose in 2-D
Particle implementation:
Motion model
  State transition based on traveled distance
  Move along roads only
  Update of sample position
Introduction | World Model | Particle Filter I | Evaluation
Particle Filter I

## Slide 6
Sensor model:
  elevation measured by a barometer
  virtual road distance measurement (always zero)
  global orientation from compass
Computation of weighting:
Introduction | World Model | Particle Filter II | Evaluation
Particle Filter II

## Slide 7
Introduction | World Model | Particle Filter II | Evaluation
Particle Filter III
Sensor Resetting
  During tracking: Insertion of samples within dynamic frame
    Compensates tracking errors
  Allows localization without known start position
    (work in progress)
Clustering
  Tracking of multiple hypotheses
  Algorithm based on resampling history

## Slide 8
Test run 1: tracking of a wheelchair
  length of test runs ~ 2.3km
  odometer readings with 2mm driving distance/tick
  magnetometer readings from Xsens MTx orientation tracker
  altimeter readings from barometer with resolution of 30.48 cm and accuracy of ±3.048m
  reference GNSS position from Garmin GPSMap 60CSx, WAAS/EGNOS enabled: positional accuracy of 3-5m in 95% of all measurements
Introduction | World Model | Particle Filter | Evaluation I
Evaluation I

## Slide 9
section 1 location: Worpswede, Germany
length: 908m
mode: tracking
section 2
location: Worpswede, Germany length: 1364m
mode: tracking
Introduction | World Model | Particle Filter | Evaluation II
Evaluation II

## Slide 10
Test run 2: tracking/global localization of a bicycle
  length of test runs ~ 40.8km
  odometer readings with 42.5cm driving distance/tick
  yaw-estimates from Xsens MTx orientation tracker, i.e. gyroscope-stabilized magnetometer
  altimeter readings from barometer with resolution of 30.48cm and accuracy of ±3.048m
  reference GNSS position from Garmin GPSMap 60CSx
Introduction | World Model | Particle Filter | Evaluation III
Evaluation III

## Slide 11
section 1
location: Osnabrück, Germany length: 10282 m
mode: tracking
section 2
location: Osnabrück, Germany length: 12186 m
mode: tracking
section 3
location: Osnabrück, Germany length: 12454 m
mode: tracking
section 4
location: Osnabrück, Germany length: 5875 m
mode: tracking
Introduction | World Model | Particle Filter | Evaluation IV
Evaluation IV

## Slide 12
section 1
location: Osnabrück, Germany length: 10282 m
mode: global localization / 10% sensor resetting (elevation)
section 2
location: Osnabrück, Germany length: 12186 m
mode: global localization / 2% sensor resetting (elevation, orientation)
Introduction | World Model | Particle Filter | Evaluation V
Evaluation V
section 3
location: Osnabrück, Germany length: 12455 m
mode: global localization / 2% sensor resetting (elevation, orientation)
section 4
location: Osnabrück, Germany length: 5875 m
mode: global localization / 10% sensor resetting (elevation)
Outlook: global localization with unknown start-position

## Slide 13
Thank you for your attention!
Questions?