## Slide 2
Introduction | Driving Assistance | Evaluation | Results
System Overview I
Basis for experimental platform:
  Power wheelchair Xeno by Otto Bock Healthcare
  Active castor wheels in the front
  CANBUS interface
Extensions:
  Two Sick S300 laser range finders
  Drive wheel encoders
  Micro controller board connects wheelchair and sensors to
  Netbook class PC

## Slide 3
Introduction | Driving Assistance | Evaluation | Results
System Overview II
Controller 1: hand joystick
  Translates hand movements into translational and rotational velocities (v, ω )
  Traditional user interface for wheelchair bound persons
  Does not suite certain disabilities, e.g. tetraplegia

## Slide 4
Introduction | Driving Assistance | Evaluation | Results
System Overview III
Controller 2: head joystick
  Head-joystick interprets pitch and roll movements of the user`s head as translational and rotational velocities (v, ω)
  Inertial measurement unit
    Cable-bound (XSens)
    Bluetooth
  Dynamic (roll) dead-zone

## Slide 5
System Overview | World Model II | Evaluation | Results
Driving Assistance I
Main concepts:
  Local occupancy grid as environmental representation

## Slide 6
System Overview | World Model II | Evaluation | Results
Driving Assistance II
Main concepts:
  Safety regions describe the breaking path, defined by:
    translational speed/acceleration (v, v’) rotational speed/acceleration (ω, ω’)
    latency of command execution
    shape of the wheelchair
    max. expected errors of measurements of v, v’, ω, ω’
    max. deceleration
    steering behavior during breaking

## Slide 7
Setup
  Course standardized by the Spanish Sport Federation for people with Cerebral Palsy
  Mimics common obstructions for wheelchair-bounded persons
Start
Start
Square of 360° turn
Start
Square of 360° turn
Figure of eight
Start
Square of 360° turn
Figure of eight
Inclines with a turn
Start
Square of 360° turn
Figure of eight
Inclines with a turn
Square for turn of 180°
Start
Square of 360° turn
Figure of eight
Inclines with a turn
Square for turn of 180°
Inversion door
System Overview | Driving Assistance | Particle Filter I | Results
Evaluation I
Start
Square of 360° turn
Figure of eight
Inclines with a turn
Square for turn of 180°
Inversion door
Goal

## Slide 8
Subjects
  Two groups of five subjects each (A/B ↔ with/without driving assistance)
  Age varies from 17 to 72 years
  Wheelchair experience ranges from none to 43 years
  Comparable impairments in A/B:
hemiparesis: weakness of one body-side
paraplegia:
impairment in motor or sensory function
ataxia:
problems coordinating muscle movement
System Overview | Driving Assistance | Particle Filter I | Results
Evaluation II

## Slide 9
Procedure
  Collect data about test person, e.g. age, gender, physical/cognitive impairments
  Ask for informed consent to evaluate data and material such as photos, etc.
  Subjects scheduled for 5 sessions
  Session comprises 30 min hand-joystick and 30 min head-joystick
  Complete obstacle stations vs. good lap times
  Log:
    controller input: v, ω
    estimated pose: x, y, θ
    number of collisions
    number of neglected, aborted, or falsely executed obstacles
System Overview | Driving Assistance | Particle Filter I | Results
Evaluation III

## Slide 10
System Overview | Driving Assistance | Particle Filter I | Results
Evaluation IV
Criteria
  Average velocity: v [m/s]
  Average number of collisions per lap: c/l
  Average number of falsely executed, aborted, disregarded obstacles per lap: e/l
  Entropy rate of controller histogram:
high clustering

low challenges
low clustering
 high challenges
number of
controller histogram
entries
probability of occurrence of controller histogram entry
Xi=(v, ω)

## Slide 11
System Overview | Driving Assistance | Particle Filter I | Results
Evaluation V
Impressions

## Slide 12
System Overview | Driving Assistance | Evaluation | Evaluation III
Results I
Findings for groups
Chart: 
| v[m/s]
Datenreihe 1 | 0.18
Datenreihe 2 | 0.14
Datenreihe 3 | 0.21
Datenreihe 4 | 0.18
hand-joystick with driving assistance | head-joystick with driving assistance
hand-joystick without driving assistance | head-joystick without driving assistance
Chart: 
| c/l
Datenreihe 1 | 0.04
Datenreihe 2 | 0.27
Datenreihe 3 | 3.07
Datenreihe 4 | 9.37
Chart: 
| e/l
Datenreihe 1 | 0.63
Datenreihe 2 | 1.2
Datenreihe 3 | 0.69
Datenreihe 4 | 1.21
Chart: 
|
Datenreihe 1 | 0.00283
Datenreihe 2 | 0.000121
Datenreihe 3 | 0.004
Datenreihe 4 | 0.00012

## Slide 13
System Overview | Driving Assistance | Evaluation | Evaluation III
Results II
Exemplary findings for individuals:
hand-joystick with driving assistance | head-joystick with driving assistance
hand-joystick without driving assistance | head-joystick without driving assistance

## Slide 14
System Overview | Driving Assistance | Evaluation | Evaluation III
Results III
Exemplary findings for individuals: hand joystick with driving assistance (A4)
Exemplary findings for individuals: hand joystick without driving assistance (B5)
Exemplary findings for individuals: head joystick with driving assistance (A5)
Exemplary findings for individuals: head joystick without driving assistance (B5)

## Slide 15
System Overview | Driving Assistance | Evaluation | Evaluation III
Results IV
Additional findings
  Diverse cognitive/motoric skills 
    High variability in adaption to non-assistive systems
    Wheelchair accessibility may not be obstructed by assistive system
  Daily physical/mental state my affect evaluation schedule
  Assistive system must indicate its state/decisions
  Test your hardware outside when you want to evaluate it outside

## Slide 16
Driving Assistance | Evaluation | Results | Evaluation III
Outlook
EU AAL JP project: Assistants for Safe Mobility
  Use of 3D environment representation addresses further classes of obstacles: holes, staircases, protruding objects, etc.
  Continue end-user centered evaluation: Bartimeus (Netherlands), Johanniter (Germany)
German Research
Center for Artificial
Intelligence GmbH

## Slide 17
Thank You!

## Slide 18
Evaluation | Results | Outlook | Evaluation III
Appendix I
Hand-Joystick trajectories - group A (with driving assistance)

## Slide 19
Hand-Joystick trajectories - group B (without driving assistance)
Evaluation | Results | Outlook | Evaluation III
Appendix II

## Slide 20
Head-Joystick trajectories - group A (with driving assistance)
Evaluation | Results | Outlook | Evaluation III
Appendix III

## Slide 21
Head-Joystick trajectories - group B (without driving assistance)
Evaluation | Results | Outlook | Evaluation III
Appendix IV

## Slide 22
Hand-Joystick controller histograms - group A (with driving assistance)
Evaluation | Results | Outlook | Evaluation III
Appendix V

## Slide 23
Hand-Joystick controller histograms - group B (without driving assistance)
Evaluation | Results | Outlook | Evaluation III
Appendix VI

## Slide 24
Head-Joystick controller histograms - group A (with driving assistance)
Evaluation | Results | Outlook | Evaluation III
Appendix VII

## Slide 25
Head-Joystick controller histograms - group B (without driving assistance)
Evaluation | Results | Outlook | Evaluation III
Appendix VIII